## Slide 1
SMART LIGHTING

## Slide 2
23
25
27
41
TEAM -
YESHWANTH
VAMSI KRISHNA
ARAVIND
TANVIKA NORI

## Slide 3
INTRODUCTION
Project Goal:
Design an automated lighting system that adjusts based on real-time environmental data.
TITLE: Smart Lighting System Using STM32F401 Black Pill
Key Features:
Uses multiple sensors for optimized, energy-efficient lighting control.
Adapts lighting based on human presence, ambient light, proximity, and temperature.
Project Relevance:
In response to the growing need for sustainable energy solutions, this project contributes to reducing energy wastage in lighting.

## Slide 4
System Components
System Components
Microcontroller: STM32F401 Black Pill
84 MHz Cortex-M4 CPU, 40 GPIO pins, 3 ADC channels.
Manages input from multiple sensors, processes data, and controls LED output.
Key Sensors:
PIR Sensor (Passive Infrared): Detects motion.
LDR (Light Dependent Resistor): Detects ambient light levels.
Ultrasonic Sensor: Measures distance to nearby objects for proximity-based lighting.
LED Indicators:
Shows real-time feedback from sensors (e.g., LDR LED, PIR LED, Ultrasonic LED).

## Slide 5
Importance of Each Sensor in the System
PIR Sensor:
Function: Detects motion to trigger lighting when movement is sensed within a specific range.
Purpose: Reduces energy usage by turning lights on only when presence is detected
LDR (Analog and Digital):
Function: Monitors light intensity in the environment.
Purpose: Automatically adjusts lighting based on ambient brightness, ensuring comfort and conserving energy during daylight.
Ultrasonic Sensor:
Function: Detects distance between people or objects and the light source.
Purpose: Adjusts brightness levels based on proximity, enhancing user experience and energy savings.
Bluetooth Sensor:
Function:
Purpose:

## Slide 6
PA1 - LDR Digital Input: Detects binary light level (on/off).
PA2 - PIR LED Output: Lights up when motion is detected by PIR.
PA3 - PIR Sensor Input: Receives motion detection input.
PA4 - Ultrasonic Trigger Output: Starts distance measurement.
PA5 - Ultrasonic Echo Input: Receives the reflected ultrasonic pulse.
PA6 - LDR LED Output: Displays ambient light detection status.
PA7 - Ultrasonic LED Output: Displays proximity detection status.
Sensor Connections and Pin Configuration
Microcontroller Pins and Sensor Mapping:

## Slide 7
Scenario Example
Scenario: Entering a Dimly Lit Room
Step 1: PIR Sensor detects your movement as you enter.
Step 2: System checks LDR; if ambient light is low, lights turn on.
Step 3: As you move closer, the Ultrasonic Sensor adjusts brightness for optimal visibility.
Benefits:
Energy Efficiency: Lights only activate when needed and adjust based on real-time conditions.
User Comfort: Light brightness adapts to distance and ambient conditions, creating a tailored lighting experience.
Convenience: Manual override provides control flexibility.

## Slide 8
Advantages of the Smart Lighting System:
Energy Savings: Automatic, sensor-driven lighting reduces unnecessary power consumption.
Enhanced User Comfort: Lighting conditions are always optimal due to proximity and ambient adjustments.
Sustainability: Reduces environmental impact by lowering overall energy usage.
Automation: Minimal user intervention required due to the integration of multiple sensors.
Conclusion:
The Smart Lighting System demonstrates an innovative solution for energy-efficient, adaptive lighting. Through real-time data from sensors, it provides a responsive lighting environment that meets user needs while conserving energy.
Key Benefits And Conclusion :